## Slide 1
Case Study of the 6-16 February 2016
Salt Lake Valley Persistent Cold-Air Pool
Sebastian W. Hoch, Erik T. Crosman, Munkh Baasandorj, Alex Jacques, John C. Lin, Ryan Bares, Randy Martin, John Sohl, John Horel, C. David Whiteman
sebastian.hoch@utah.edu
2016 AMS Mtn. Met.
Burlington, VT

## Slide 2
The Salt Lake City basin is one of the three populated Utah valleys marked as non-attainment areas for PM2.5 pollution (UDEQ, 2015)
Adverse health effects of the PM2.5 are well documented, both for short term and long term exposure (adverse birth outcome, asthma, heart disease, heart attacks, chronic obstructive pulmonary disease).
Chemical composition of PM2.5 pollution in Utah valleys shows high mass contribution of Ammonium Nitrate (NH4NO3; 70-80%), and Ammonium Chloride (NH4Cl; 10-15%) (Kelly et al. 2013; Kuprov et al. 2014)
Ammonium Nitrate (NH4NO3) is a ”secondary pollutant” forming from gaseous ammonia (NH3) and nitric acid (HNO3).
Background (1)
SLC, UT. 14 Jan 2011

## Slide 3
Background (2)
The (somewhat) known:
Wintertime pollution episodes are closely linked to persistent cold-air pools (PCAPs).
Heat deficit concept is very useful.
The life cycle of PCAPs and their dependence on meteorological processes has previously been investigated (PCAPS, COLPEX,…)
The less known:
The reactive pathways for NH4NO3 formation are unknown.
Very little is known about the spatial variation of PM2.5 concentrations and precursor gases within a PCAP.
Temporal variations (on timescales < 24 hours) are unknown.
Lareau et al. 2013, BAMS; Lareau and Horel 2015, BLM; Lareau and Horel 2015, JAS; Holmes et al. 2015, EST; Crosman and Horel 2016, BLM; Price et al. 2011, BAMS; …
Whiteman et al. 2014, Atmos. Env.

## Slide 4
The Wintertime PM2.5 Air Pollution Study (2015/16)
The Utah Department of Environmental Quality (UDEQ) funded a study to investigate the links between chemical and meteorological processes under PCAP conditions.
Chemistry:
Identify the dominant reactive pathways of NH4NO3 formation.
Meteorology:
Characterize persistent wintertime cold air pools (PCAPs) associated with pollution episodes.
Chemistry – Meteorology Connections:
Investigate the meteorological processes that modulate the temporal and spatial pollutant concentrations under PCAP conditions?
Ammonium nitrate
hν,NO
hν
NO
NO2
NO2
NO3
N2O5
M
O3
NH3
HNO3
Ammonia
HNO3
Nitric acid
OH, M
H2O
Het. uptake
HONO

## Slide 5
Wasatch Range
Oquirrh Mtns.
Traverse Range
Great
Salt
Lake
~30 km
The Salt Lake City Basin
Google Earth Image

## Slide 6
Experimental Design
PM 2.5 and Chemistry
TEOM
Aerosol Backscatter
Temperature and Wind profile
NWS
Radiosonde
UU
Wind Lidar
Pseudovertical
Transect

## Slide 7
Mobile Platforms
Logan Mitchell, Ben Fasoli, Alex Jacques, Luke Leclair-Marzolf
Chopper

## Slide 8
The 2015-2016 Cold Season
Valley Heat Deficit and PM2.5
4 Jan.
7 – 14 Feb.
9 Exceedances (typically 18) of the NAAQS of 35 μg/m3
NAAQS
(2200 m MSL)
(1300 m MSL)
(below 2200 m MSL)

## Slide 9
Temporal variations
“Clear”
“Haze/Fog”
Daily increase by ~10-15 μg/m3
(Whiteman et al. 2014: 10 μg/m3 )
Constant level of ~60 μg/m3
(Whiteman et al. 2014: 60 μg/m3 )
Results

## Slide 10
“Clear”
“Haze/Fog”
Temperature Structure 6-16 February 2016
Nocturnal strengthening of CAP
Daytime heating & mixing
Dampening of diurnal cycle
Lowest 400 m remain “well mixed”

## Slide 11
Chopper
1) Takeoff
2) Dip-down
South SLC
3) Dip-down
Utah Basin
4) Landing
9 Feb. 2016
~1 Hour flight
Results – Spatial Variations (vertical)

## Slide 12
North Salt
Lake Basin
North Salt
Lake Basin
Utah
Basin
South Salt
Lake Basin
Spatial Variations : News Helicopter Flight 9 Feb. 2016
Salt Lake City Basin
Utah Basin

## Slide 13
Tributary canyons, down-canyon flows, and air quality
Red Butte
Hawthorne
U. of Utah
NAA
ENE down-canyon flow
Cleaner air at mouth of Red Butte Canyon

## Slide 14
5 km

## Slide 15
Clean air injection – Center of Basin – Ceilometer / Lidar
09 February case
Clean-air injections into CAP!

## Slide 16
σw (vertical velocity variance) from Lidar stares shows convection at the base of the CAP
Pollution is ejected along the sidewalls into elevated layers and advected with the weak mean flow. Ventilation
Daytime heating – Upslope flows – Aerosol layering?
σw contours

## Slide 17
Aerosol formation (?)

## Slide 18
NO2
Chemistry
Nighttime Chemistry (N2O5 )
Early Morning – Post Sunrise Production

## Slide 19
Summary / Conclusions
A lot more than expected is happening in a Persistent Cold Air Pool!
Air mass exchanges between sub-basins, and with the lake boundary layer modulate pollutant concentrations.
Down-canyon flows bring cleaner air to the mouths of the canyons at night.
Cleaner air is also observed at elevated levels within the CAP at night. Clean air injections (at night) may trigger NH4NO3 formation (O3 injection).
Vertical mixing – even under CAP conditions – leading to upward mixing of pollutants.
Ventilation processes are indicated along the basin sidewalls during daytime (ejections / formation of elevated pollutant layers).
Two processes are indicated to lead to HNO3 (and therefore NH4NO3) formation.

## Slide 20
Acknowledgements
Funding: Utah Division for Environmental Quality
All PI’s, students and volunteers involved in the project!

## Slide 21
Additional Slides

## Slide 22
Southerly flow through Jordan Narrows diluting pollutants south to north.
Flow weakens and is replaced by weak afternoon up-valley / lake breeze flow.
+1 to +4 C
- 4 to -1 C
Flow through gap
~6 m/s
1-2 m/s
calm
+3 to +4 C
+5 to +6 C
+3 to +4 C
1-2 m/s
1-2 m/s
Results – Spatial Variations (horizontal)

## Slide 23
Valley Heat Deficit 6-16 February 2016
“Clear”
“Haze/Fog”
r = 0.64
r = 0.60
r = 0.67

## Slide 24
TRAX
Results – Spatial Variations (horizontal)
Canyon exits areas and
Salt Lake Basin “benches” often show reduced PM2.5 concentrations.

## Slide 25
TRAX
Results – Spatial Variations (horizontal)

## Slide 26
σw
σw
σw
Mixing  lowering of near-surface concentrations
 lofting of pollutants.

## Slide 27
Chemistry

## Slide 28
Aerosol Backscatter 6-16 February 2016
“Clear”
“Haze/Fog”

## Slide 29
Daytime
OH + NO2 HNO3 (sunlight!)
Nighttime
NO2 + O3 NO3 + O2
NO3 + NO2 + M N2O5
N2O5 +H2O(l) 2 HNO3
We have plenty of NO2 !
We need Ozone O3 !
O3 is titrated !
NO + O3 NO2+O2
Daytime – Chlorine ClNO2 radical ? Photochemical activation – OH- …
If too much NO then NO reacts with NO3,
Preventing

## Slide 30
Outline
Background (why; problem; what we know)
Approach (What we don’t know and how we’re trying to find out more)
SLC basin
Instrumentation
Mobile Instrumentation
Winter 2015/2016
The 6-16 February episode
Backscatter
Heat Deficit (diurnal)
Temperature Structure (Hobos)
Transition profiles
Results:
Variations
1. Temporal:
2. Spatial:
Trax:
a) Cleaner benches
b) Spatial gradients (Lake Breeze / partial mix-out )
Topography effects
Nighttime: Canyon Inflows
Nightime: Cold air injections (in cold pool)
c) Daytime: Upslope ejection
Chemistry: Two types of chemistry (nighttime / early morning)