## Slide 1
Temperature datalogger lines during PCAPS
Sebastian Hoch, Dave Whiteman & all PCAPS participants

## Slide 2
Motivation
Key feature of Cold Air Pools is the vertical temperature profile.
Quasi-vertical profiles can be obtained by observations along mountain slopes.
Advantages: cheaper than radiosondes, continuous measurements.
Disadvantages: Local boundary layer influences need to be taken into account

## Slide 3
Objectives
How do the characteristics of the inversions (height, strength, intensity ... ) vary spatially & temporally?
What are and what can we learn about the processes responsible for the variations?

## Slide 4
Choice of instrument – The HOBO
Inexpensive automatic temperature dataloggers (Onset Computers)
Thermistor with ~3 min response time
Mounted in radiation shields
Fastened to fence posts
Well tested in previous studies

## Slide 5
Grandeur Line
Kennecott Line
Harker’s Line
85 HOBOs available
Instrument all 50-m elevation contours up to 2500 m
West and East slope of the Salt Lake basin (Harker’s vs. Grandeur Line)
Northern and Southern part of the valley (Harker’s vs. Kennecott Line)
Experimental
design

## Slide 6
There is a good correspondence between logger-lines and with radiosonde data during high-wind conditions.
Preliminary results – Comparison with Radiosondes

## Slide 7
2) Spatial variations in vertical profile exist and are resolved

## Slide 8
3) Differences in profiles - due to local processes?
HOBO-T-profile over low slope angle sites is cooler than radiosonde profile
Local nocturnal cooling effects likely.
Case 1:
Night of 1-2 December
Clear night with strong surface cooling
~ 10 PM 1 Dec.
~ 05 AM 2 Dec.
Low slope angle
Low slope angle

## Slide 9
Case 2:
2-3 December:
Strong southerly winds (~15 m/s).
Pronounced temperature differences at different heights
Warmer air aloft in basin center
“Mix-out” of the inversion in southern part of the valley.
Downslope warming?
Partial mix-out of valley inversion

## Slide 10
5 Dec 1600 MST
1-3 December: Shortwave Ridge building (peak 5 pm 2 Dec)
3 December: Short wave trough glancing by: precipitation & strong westerly flow
Partial mix-out in southern part of valley
4 December: Isothermal structure
5 December: Fog
5-6 December: Upper level clouds dissipate – strong cooling on fog / low cloud top
7 December: Mix-out
4) IOP-1 in all its complexity as seen by the HOBOs
7 Dec 0800 MST
2 Dec 1000 MST
3 Dec 1130 MST
... but first a short summary:

## Slide 12
Lowering subsidence inversions
Spatial differences in “mix-out” events
Downslope warming
Evaporative cooling
Cloud-(Fog)-Top cooling
Differential heating due to snow cover & insolation differences
Lake breeze surges
Sloshing & seiches ?
Summary
The HOBO temperature data logger lines give continuous quasi-vertical temperature profiles
Local effects are seen in the data
Valley inversions are very dynamic and constantly evolving
Phenomena seen in HOBO temperature signatures comprise:

## Slide 13
Acknowledgements
Siting of HOBOs – Thanks for giving a HOBO a home:
National Forest Service (Carol Majeske)
Rio Tinto / Kennecott Land (Chris Kaiser / Jeff Lachowski)
All the local businesses and private people that allowed a placement of a temperature sensor on their property!
Placing of HOBOs – Thanks for dealing cutting straws & with steep muddy and slopes heavy fence post pounders
HOBO-Party participants & hosts
Hiking & hauling friends